## Slide 1: Read module

## Slide 2: System Initialization
When reseted read cycles are executed to populate L1 cache.
1)Selects target
2)Push address to ADDR bus
3) AR, wait for DR active
4) Data read from MM on Data bus ready
5)Update cache lines
6)Follow private bus per snoop by other CPU

## Slide 3
SLCK (System Lock) : To indicate a processor that the other is going to execute a bus read
PINV(Write/read cycle): asserted low by the processor doing a read cycle.
DR: data on data bus ready

## Slide 4: Bus read cycle sequence
In the MRM the processor should wait for the signal SLCK to be deasserted and then PLCK to take control and start the read cycle
MRM asserts AR and SLCK to LRM
SNOOP on LRM if not there on external memory
When data ready from any DR to MRM to indicate completion of the cycle
The processor doesnt releases the control of the bus when executing a read cycle
Performed when a miss occurs

## Slide 5
INVALID
Read miss, line fill(WB/WT# = 0) change to SHARED
Read miss, line fill(WB/WT#=1) change to exclusive
SHARED
Read hit or external snoop hit on read(WB/WT#=0) Stays on SHARED
EXCLUSIVE
External snoop hit on read, changes to SHARED
Read hit, stays on EXCLUSIVE
Modified
Read hit, stays on modified
Write back: external snoop hit on read changes to SHARED

## Slide 6: Snoop results- reads
Miss: line not catched in LRM, keeps PHIT# and PHITM# deasserted. MRM completes memory read an stores line in E state
Hit Clean: line in LRM in E or S, asserts PHIT# only. Line changes to S or maintains in S. MRM comletes memory read and stores line in S state.
Hit Modified: line in LRM but modified, PHIT# and PHITM# asserted.LRM and MRM switch for memory write back, and switches again for memory read. Line changes from M to S.

## Slide 7
MRM/LRM snoop miss: not cached in any, both miss, HIT# and HITM# deasserted. Bus master completes memory read
MRM HIT LRM MISS: Line cached in MRM( S or E, E changes to S). MRM hit# only asserted.
MRM MISS LRM HIT: line cached in LRM(“) LRM hit#, then MRM HIT# to notify system
MRM HIT LRM HIT: LINE CACHED ON BOTH(S) both report hit#
MRM HITM LRM MISS: LINE CACHED ONLY IN MRM, REPORTS HIT# AND HITM#, takes control of bus and procedes write back, after write back, hit and hitm deasserted and bus control for the bus master to complete memory read
MRM MISS LRM HITM: LINE CACHED IN LRM, REPORTS HIT AND HITM, ALSO MRM AND TAKES CONTROL OF BUS, LRM ASSERTS PBREQ# TO REQUEST BUS TO PERFORM WRITEBACK( M TO S) MRM GRANTS BY PBGNT#. MRM AND LRM SWITCH. NEW MRM WRITES TO MEMORY. AFTER IT HIT AND PHIT DEASSERTED(ORIGINAL LRM) ALSO LRM. Bus is released for the bus master to complete memory read.

## Slide 8
MRM Asserts CACHE# when it initiates cache line read or write-back of modified line, LRM latches CACHE#

## Slide 9: Memory Addresing
RW bit : read cycle when asserted